User’s Guide

GDM12864A ™ LCM

(Liquid Crystal Display Module)

XIAMEN OCULAR LCD DEVICES CO., LTD.

厦门高卓立液晶显示器有限公司

South 5F., Guang Xia Bldg. Torch Hi-tech

Develop. Area, Xiamen, China 361006

Tel: (0592)6026045	Fax: (0592)6026021

Contents

Chapter 1.  Introduction to GDM-12864A LCM		              1

Features					    1

Mechanical Specifications		    1

Temperature Characteristics		    1

External Dimensions			    2

Application Diagram			    3

Electro- Optical characteristics	    4

Interface Pin Connections		    5

Electrical Absolute Maximum Rating (KS0107B)		6

DC Electrical Characteristics (KS0107B)				6

Electrical Absolute Maximum Rating (KS0108B)		7

DC Electrical Characteristics (KS0108B)				7

Chapter 2.  Driver IC (KS0107B) Function Description			8

Introduction						8

AC Characteristics 				9

Master Mode					9

Slave Mode						10

Functional Description				11

RC Oscillator					11

Timing Generation Circuit			11

Data Shift & Phase Select Control	12

Chapter 3.  Driver IC (KS0108B) Function Description			13

Introduction						13

AC Characteristics 				13

Operating Principles & Methods		16

Display Control Instruction			19

CHAPTER 1

Introduction to ITM-12864A LCM

GDM12864A is a dot matrix graphic LCD module which is fabricated by low power COMS technology. It can display 128*64 dots size LCD panel using a 128*64 bit-mapped Display Data RAM (DDRAM). It interfaces with an 8-bit microprocessor.

Features

- Display format: 128*64 dots matrix graphic

- STN yellow-green mode

- Easy interface with 8-bit MPU

- Low power consumption

- LED back-light

- Viewing angle: 6 O’clock

- Driving method : 1/64 duty , 1/6.7 bias

- LCD driver IC: KS0108B(2个)、KS0107B

- Connector: Zebra

Mechanical Specifications

| Item | Dimension | Unit |
| --- | --- | --- |
| Module Size(W*H*T) | 93.0*70.0*10.0 | mm |
| Viewing Area(W*H) | 72.0*40.0 | mm |
| Number of Dots | 128.0*64.0 | PCS |
| Dot Size(W*H) | 0.48*0.48 | mm |
| Dot Pitch(W*H) | 0.52*0.52 | mm |
| Module Size With B/L | 93.0*70.0*15.0 | mm |

Temperature Characteristics

| Parameter | Symbol | Rating | Unit |
| --- | --- | --- | --- |
| Operating temperature | Topr | 0 ~ +50 | ℃ |
| Storage temperature | Tstg | -20 ~ +70 | ℃ |

Figure 1. External Dimensions

| PIN | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SIGNAL | Vss | VDD | V0 | D/I | R/W | E | DB0 | DB1 | DB2 | DB3 |
| PIN | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 |
| SIGNAL | DB4 | DB5 | DB6 | DB7 | CS1 | CS2 | RES | VEE | A | K |

*NOTE:  1.All units are mm.

2.Tolerances unless otherwise specified (0.2.

Figure 2. Application Diagram

*Note

1/64 duty, 1/6.7 bias

VDD>V1>V2>V3>V4>V5>VEE

Electro-Optical characteristics

TN Type (Twisted Nematic )

| Item | Symbol | Min. | Typ. | Max. | Unit | Condition | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Viewing Angle | θ2 -θ1 | 40 | - | - | deg. | Cr = 2.0 | 1,2 |
|  | φ |  |  |  |  |  |  |
| Contrast Ratio | Cr | - | 4 | - | - | θ=20ο φ= 0ο | 3 |
| Response Time (rise) | tR | - | 110 | - | ms | θ=20ο φ= 0ο | 4 |
| Response Time (fall) | tF | - | 110 | - | ms | θ=20ο φ= 0ο | 4 |

STN Type (Super Twisted Nematic )

| Item | Symbol | Min. | Typ. | Max. | Unit | Condition | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Viewing Angle | θ2 -θ1 | 70 -90 | - | +90 | deg. | Cr = 2.0 | 1,2 |
|  | φ |  |  |  |  |  |  |
| Contrast Ratio | Cr | - | 4 | - | - | θ=20ο φ= 0ο | 3 |
| Response Time (rise) | tR | - | 110 | - | ms | θ=20ο φ= 0ο | 4 |
| Response Time (fall) | tF | - | 110 | - | ms | θ=20ο φ= 0ο | 4 |

Interface Pin Connections

| Pin No. | Symbol | I/O Type | Description |
| --- | --- | --- | --- |
| 1 | VSS | Supply | Ground |
| 2 | VDD | Supply | Power supply |
| 3 | V0 | Supply | LCD driver supply voltage |
| 4 | D/I |  | Data input/output pin of internal shift register MS SHL DIO1 DIO2 H H Output Output H L Output Output L H Input Output L L Output Input |
| 5 | R/W |  | Read or Write RW Description H Data appears at DB[7:0] and can be read by the CPU while E= H CS1B=L,CS2B=L and CS3=H. L Display data DB[7:0] can be written at falling edge of E when CS1B=L, CS2B=L and CS3=H. |
| 6 | E |  | Enable signal E Description H Read data in DB[7:0] appears while E= “High”. L Display data DB[7:0] is latched at falling edge of E. |
| 7 | DB0 | I/O | Data bus [0~7] Bi-directional data bus |
| 8 | DB1 |  |  |
| 9 | DB2 |  |  |
| 10 | DB3 |  |  |
| 11 | DB4 |  |  |
| 12 | DB5 |  |  |
| 13 | DB6 |  |  |
| 14 | DB7 |  |  |
| 15 16 | CS1 CS2 | I | Chip selection When CS1=H,CS2=L, select IC1 When CS1=L,CS2=H, select IC2 |
| 17 | RESETB | I | Reset signal. When RSTB=L 【1】ON/OFF register becomes set by 0.(display off) 【2】display start line register becomes set by 0 (Z-address 0 set, display from line 0) 【3】After releasing reset , this condition can be changed only by instruction. |
| 18 | VEE | Power | VEE is connected by the same voltage. |
| 19 | A |  | Back-light anode |
| 20 | K |  | Back-light cathode |

Electrical Absolute Maximum Ratings (KS0107B)

| Parameter | Symbol | Rating | Unit | Note |
| --- | --- | --- | --- | --- |
| Operating voltage | VDD | -0.3 ~ +7.0 | V | *1 |
| Supply voltage | VEE | VDD-19.0 ~ VDD+0.3 | V | *4 |
| Driver supply voltage | VB | -0.3 ~ VDD+0.3 | V | *1,2 |
|  | VLCD | VEE-0.3 ~ VDD+0.3 | V | *3,4 |

*Notes:

- Based on VSS = 0V

- Applies to input terminals and I/O terminals at high impedance. (Except V0L, V1L, V4L, and V5L)

- Applies to V0L, V1L, V4L, and V5L.

- Voltage level: VDD≥V0≥V1≥V2≥V3≥V4≥V5≥VEE

DC Electrical Characteristics(KS0107B)

(VDD= 4.5 to 5.5V, VSS=0V,VDD-VEE=8~17V,Ta= -30 to +85℃)

| Item | Symbol | Condition | Min. | Typ. | Max. | Unit | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Operating voltage | VDD | - | 4.5 | - | 5.5 | V |  |
| Input voltage | VIH | - | 0.7VDD | - | VDD |  | *1 |
|  | VIL | - | VSS | - | 0.3VDD |  |  |
| output voltage | VOH | IOH= -0.4mA | VDD-0.4 | - | - |  | *2 |
|  | VOL | IOL= 0.4mA | - | - | 0.4 |  |  |
| Input leakage current | ILKG | VIN= VDD ~ VSS | -1.0 | - | +1.0 | (A | *1 |
| OSC Frequency | fosc | Rf=47kΩ±2% Cf=20pF±5% | 315 | 450 | 585 | kHz |  |
| On Resistance (Vdiv-Ci) | RONS | VDD-VEE=17V Load current±150(A | - | - | 1.5 | kΩ |  |
| Operating current | IDD1 | Master mode 1/128 Duty | - | - | 1.0 | mA | *3 |
|  | IDD2 | Master mode 1/128 Duty | - | - | 0.2 |  | *4 |
| Supply Current | IEE | Master mode 1/128 Duty | - | - | 0.1 |  | *5 |
| Operating | fop1 | Master mode External Duty | 50 | - | 600 | kHz |  |
| Frequency | fop2 | Slave mode | 0.5 | - | 1500 |  |  |

Notes

- Applies to input terminals FS, DS1, DS2, CR, SHL, MS and PCLK2 and I/O terminals DIO1, DIO2, M , and CL2 in the input state.

- Applies to output terminals CLK1, CLK2 and FRM and I/O terminals DIO1, DIO2, M , and CL2 in the output state.

- This value is specified about current flowing through VSS.

Internal oscillation circuit: Rf=47kΩ, cf=20pF

Each terminals of DS1, DS2, FS, SHL, and MS is connected to VDD and out is no load.

- This value is specified about current flowing through VSS.

Each terminals is DS1, DS2, FS, SHL, PCLK2 and CR is connected to VDD,MS is connected to VSS

and CL2, M, DIO1 is external clock.

*5. This value is specified about current flowing through VEE, Don’t connect to VLCD (V1~V5).

Electrical Absolute Maximum Ratings(KS0108B)

| Parameter | Symbol | Rating | Unit | Note |
| --- | --- | --- | --- | --- |
| Operating voltage | VDD | -0.3 ~ +7.0 | V | *1 |
| Supply voltage | VEE | VDD-19.0 ~ VDD+0.3 | V | *4 |
| Driver supply voltage | VB | -0.3 ~ VDD+0.3 | V | *1,3 |
|  | VLCD | VEE-0.3 ~ VDD+0.3 | V | *2 |

*Notes:

- Based on VSS = 0V

- Applies the same supply voltage to VEE. VLCD=VDD-VEE.

- Applies to M, FRM, CLK1,CLK2, CL, RESETB, ADC, CS1B, CS2B,CS3, E, R/W, RS and DB0~DB7.

- Applies V0L,V2L,V3L and V5L.

Voltage level: VDD≥V0≥V1≥V2≥V3≥V4≥V5≥VEE

DC Electrical Characteristics(KS0108B)

(VDD= 4.5 to 5.5V, VSS=0V,VDD-VEE=8~17V,Ta= -30 to +85℃)

| Item | Symbol | Condition | Min. | Typ. | Max. | Unit | Note |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Operating voltage | VDD | - | 4.5 | - | 5.5 | V |  |
| Input High voltage | VIH1 | - | 0.7VDD | - | VDD |  | *1 |
|  | VIH2 | - | 2.0 | - | VDD |  | *2 |
| Input Low voltage | VIL1 | - | 0 | - | 0.3VDD |  | *1 |
|  | VIL2 | - | 0 | - | 0.8 |  | *2 |
| Output High Voltage | VOH | IOH= -0.2mA | 2.4 | - | - |  | *3 |
| Output Low Voltage | VOL | IOL= 1.6mA | - | - | 0.4 |  | *3 |
| Input leakage current | ILKG | VIN= VSS ~ VDD | -1.0 | - | +1.0 | (A | *4 |
| Three-state (OFF) Input Current | ITSL | VIN= VSS ~ VDD | -5.0 | - | 5.0 |  | *5 |
| Driver Input leakage current | IDIL | VIN= VEE ~ VDD | -2.0 |  | 2.0 |  | *6 |
| On Resistance (Vdiv-Ci) | RONS | VDD-VEE=15V Load current±100(A | - | - | 7.5 | kΩ | *8 |
| Operating current | IDD1 | During Display | - | - | 0.1 | mA | *7 |
|  | IDD2 | During Access Access Cycle=1MHz | - | - | 0.5 |  | *7 |

Notes

- CL, FRM, M, RSTB, CLK1, CLK2

- CS1B, CS2B, CS3, E, R/W, RS, DB0~DB7

- DB0~DB7

- Except DB0~DB7

- DB0~DB7 at high impedance

- V0, V1, V3, V3, V4, V5

- 1/64 duty , FCLK=250KHZ, Frame Frequency=70HKZ, Output: No Load

- VDD-VEE=15.5V

V0L>V2L>= VDD-2/7(VDD-VEE)>V3L= VEE+2/7(VDD-VEE)>V5L

CHAPTER 2

Driver IC Function Description

KS0107 Driver IC

64COM graphic driver for dot matrix LCD

Introduction

The KS0107B is an :CD driver LSI with 64 channel outputs for dot matrix liquid crystal graphic display systems.

This device provides 64 shift registers and 64 output drivers.

It generates the timing signal to control the KS0108B (64 channel segment drover.).

The KS0107B is fabricated by low power CMOS high voltage process technology, and is composed of the liquid crystal display system in combination with the KS0108B (64 channel segment drover.).

AC Characteristics (VDD=4.5~5.5V, Ta=-30℃~+85℃)

1. Master mode (MS=VDD, PCLK2=VDD, Cf=20pF, Rf=47KΩ)

| Characteristic | Symbol | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- |
| Data Setup Time | tSU | 20 | - | - | (s |
| Data Hold Time | tDH | 40 | - | - |  |
| Data Delay Time | tD | 5 | - | - |  |
| FRM Delay Time | tDF | -2 | - | 2 |  |
| M Delay Time | tDM | -2 | - | 2 |  |
| CL2 Low Level Width | tWLC | 35 | - | - |  |
| CL2 High Level Width | tWHC | 35 | - | - |  |
| CLK1 Low Level Width | tWL1 | 700 | - | - | ns |
| CLK2 Low Level Width | tWL2 | 700 | - | - |  |
| CLK1 High Level Width | tWH1 | 2100 | - | - |  |
| CLK2 High Level Width | tWH2 | 2100 | - | - |  |
| CLK1-CLK2 Phase Difference | tD12 | 700 | - | - |  |
| CLK2-CLK1 Phase Difference | tD21 | 700 | - | - |  |
| CLK1,CLK2 Rise/Fall Time | tR/t F | - | - | 150 |  |

Slave mode (MS=VSS)

| Characteristics | Symbol | Min | Typ | Max | Unit | Note |
| --- | --- | --- | --- | --- | --- | --- |
| CL2 Low Level Width | tWLC1 | 450 | - | - | ns | PCLK2=VSS |
| CL2 High Level Width | tWHC1 | 150 | - | - |  | PCLK2=VSS |
| CL2 Low Level Width | tWLC2 | 150 | - | - |  | PCLK2=VDD |
| CL2 High Level Width | tWHL | 450 | - | - |  | PCLK2=VDD |
| Data Setup Time | tSU | 100 | - | - |  |  |
| Data Hold Time | tDH | 100 | - | - |  |  |
| Data Delay Time | tD | - | - | 200 |  | *1 |
| Output Data Hold Time | tH | 10 | - | - |  |  |
| CL2 Rise/Fall Time | tR/tF | - | - | 30 |  |  |

*1: Connect load CL=30pF

FUNCTIONAL DESCRIPTION

- RC Oscillator

The RC Oscillator generates CL2, M, FRM, of the KS0107B and CLK1, CLK2 of the KS0107B by the oscillation resister R and capacitor C.

When selecting the master/slave, oscillation circuit is as following:

- Master Mode

- Slave Mode

- Timing Generation circuit

It generates CL2, M, FRM, CLK1, and CLK2 by the frequency from oscillation circuit.

- Selection of Master/Slave (M/S) 
When M/S is “H”, it generates CL2, M, FRM, CLK1, and CLK2 internally. When M/S is “L”, it operates by receiving M, CLK2 from master device.

- Frequency Selection (FS)
To adjust FRM by 70Hz, the oscillation frequency should be as following:

| FS | Oscillation Frequency |
| --- | --- |
| H | fOSC=430KHz |
| L | fOSC=215KHz |

In the slave mode, it is connected to VDD.

- Duty Selection (DS1, DS2)
It provides various duty selection according to DS1, DS2.

| DS1 | DS2 | DUTY |
| --- | --- | --- |
| L | L | 1/48 |
|  | H | 1/64 |
| H | L | 1/96 |
|  | H | 1/128 |

- Data shift & Phase Select Control

- Phase Selection
It is a circuit to shift data on synchronization or rising edge or falling edge of the CL2 according to PCLK2.

| PCLK2 | Phase Selection |
| --- | --- |
| H | Data shift on rising edge of CL2 |
| L | Data shift on falling edge of CL2 |

- Data shift Direction Selection 
When M/S is connected to VDD, DIO1 and DIO2 terminal is only output.
When M/S is connected to VSS, it depends on the SHL.

| MS | SHL | DIO1 | DIO2 | Direction of Data |
| --- | --- | --- | --- | --- |
| H | H | Output | Output | C1~C64 |
|  | L | Output | Output | C64~C1 |
| L | H | Input | Output | DIO1~C1~C64~DIO2 |
|  | L | Output | Input | DIO2~C64~C1~DIO1 |

CHAPTER 3

Driver IC Function Description

KS0108 Driver IC

64 SEG graphic driver for dot matrix LCD

Introduction

The KS0108B is an LCD driver LSI with 64 channel outputs for dot matrix liquid crystal graphic display systems. This device consists of the display RAM, 64 bit data latch 64 bit drivers and decoder logics. It has the internal display RAM for storing the display data transferred from a 8 bit micro controller and generates the dot matrix liquid crystal driving signals corresponding to stored data. The KS0108B composed of the liquid crystal display system in combination with the KS0107B(64 common driver).

AC Characteristics (VDD=4.5~5.5V ,VSS=0V, Ta=-30℃~+85℃)

- Clock Timing

| Characteristic | Symbol | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- |
| CLK1, CLK2 Cycle Time | tCY | 2.5 | - | 20 | (s |
| CLK1‘LOW’Level Width | tWL1 | 625 | - | - | ns |
| CLK2‘LOW’Level Width | tWL2 | 625 | - | - |  |
| CLK1‘HIGH’Level Width | tWH1 | 1875 | - | - |  |
| CLK2‘HIGH’Level Width | tWH2 | 1875 | - | - |  |
| CLK1-CLK2 Phase Difference | tD12 | 625 | - | - |  |
| CLK2-CLK1 Phase Difference | tD21 | 625 | - | - |  |
| CLK1, CLK2 Rise Time | tR | - | - | 150 |  |
| CLK1, CLK2 Fall Time | tF | - | - | 150 |  |

（2）.Display Control Timing

| Characteristic | Symbol | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- |
| FRM Delay Time | tDF | -2 | - | 2 | us |
| M Delay Time | tDM | -2 | - | 2 |  |
| CL ‘LOW’Level Width | tWL | 35 | - | - |  |
| CL‘HIGH’Level Width | tWH | 35 | - | - |  |

（3）. MPU Interface

| Characteristic | Symbol | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- |
| E Cycle | tC | 1000 | - | - | ns |
| E High Level Width | tWH | 450 | - | - |  |
| E Low Level Width | tWL | 450 | - | - |  |
| E Rise Time | tR | - | - | 25 |  |
| E Fall Time | tF | - | - | 25 |  |
| Address Set-Up Time | tASU | 140 | - | - |  |
| Address Hold Time | tAH | 10 | - | - |  |
| Data Set-Up Time | tSU | 200 | - | - |  |
| Data Delay Time | tD | - | - | 320 |  |
| Data Hold Time (Write) | tDHW | 10 | - | - |  |
| Data Hold Time (Read) | tDHR | 20 | - | - |  |

OPERATING PRINCIPLES & METHODS

- I/O Buffer
Input buffer controls the status between the enable and disable of chip. Unless the CS1B to CS3 is in active mode, Input or output of data and instruction does not execute. Therefore internal state is not change. But RSTB and ADC can operate regardless CS!B-CS3.

- Input register
Input register is provided to interface with MPU which is different operating frequency. Input register stores the data temporarily before writing it into display RAM.
When CS1B to CS3 are in the active mode, R/W and RS select the input register. The data from MPU is written into input register. Then writing it into display RAM. Data latched for falling of the E signal and write automatically into the display data RAM by internal operation.

Output register
Output register stores the data temporarily from display data RAM when CS1B, CS2B and CS3 are in active mode and R/W and RS=H, stored data in display data RAM is latched in output register. When CS1B to CS3 is in active mode and R/W=H , RS=L, status data (busy check) can read out.
To read the contents of display data RAM, twice access of read instruction is needed. In first access, data in display data RAM is latched into output register. In second access, MPU can read data which is latched. That is to read the data in display data RAM, it needs dummy read. But status read is not needed dummy read.

| RS | R/W | Function |
| --- | --- | --- |
| L | L | Instruction |
|  | H | Status read (busy check) |
| H | L | Data write (from input register to display data RAM ) |
|  | H | Data read (from display data RAM to output register) |

- Reset
The system can be initialized by setting RSTB terminal at low level when turning power on, receiving instruction from MPU. When RSTB becomes low, following procedure is occurred.
1. Display off
2. Display start line register become set by 0.(Z-address 0)
While RSTB is low, No instruction except status read can by accepted. Therefore, execute other instructions after making sure that DB4= (clear RSTB) and DB7=0 (ready) by status read instruction.
The conditions of power supply at initial power up are shown in table 1.

Table 1. Power Supply Initial Conditions

| Item | Symbol | Min | Typ | Max | Unit |
| --- | --- | --- | --- | --- | --- |
| Reset Time | tRS | 1.0 | - | - | us |
| Rise Time | tR | - | - | 200 | ns |

- Busy flag

Busy flag indicates that KS0108B is operating or no operating. When busy flag is high, KS0108B is in internal operating .
When busy flag is low, KS0108B can accept the data or instruction.
DB7indicates busy flag of the KS0108B.

- Display On/Off Flip-Flop

The display on/off flip-flop makes on/off the liquid crystal display. When flip-flop is reset (logical low), selective voltage or non selective voltage appears on segment output terminals. When flip-flop is set (logic high), non selective voltage appears on segment output terminals regardless of display RAM data.
The display on/off flip-flop can changes status by instruction. The display data at all segment disappear while RSTB is low.
The status of the flip-flop is output to DB5 by status read instruction.
The display on/off flip-flop synchronized by CL signal.

- X Page Register
X page register designates pages of the internal display data RAM.
Count function is not available. An address is set by instruction.

- Y address counter
Y address counter designates address of the internal display data RAM. An address is set by instruction and is increased by 1 automatically by read or write operations of display data.

- Display Data RAM
Display data RAM stores a display data for liquid crystal display. To indicate on state dot matrix of liquid crystal display , write datra1. The other way , off state, writes 0.
Display data RAM address and segment output can be controlled by ADC signal.
ADC=H => Y-address 0: S1~Y address 63: S64
ADC=L => Y-address 0: S64~Yaddress 63: S1
ADC terminal connect the VDD or VSS.

- Display Start Line Register
The display start line register indicates of display data RAM to display top line of liquid crystal display.
Bit data (DB<0.5>) of the display start line set instruction is latched in display start line register. Latched data is transferred to the Z address counter while FRM is high, presetting the Z address counter.
It is used for scrolling of the liquid crystal display screen.

Display Control Instruction

The display control instructions control the internal state of the KS0108B. Instruction is received from MPU to KS0108B for the display control. The following table shows various instructions.

| Instruction | RS | RW | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 | Function |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Read Display Date | 1 | 1 | Read data | Reads data (DB[7:0]) from display data RAM to the data bus. |
| Write Display Date | 1 | 0 | Write data | Writes data (DB[7:0]) into the DDRAM. After writing instruction, Y address is incriminated by 1 automatically |
| Status Read | 0 | 1 | Busy | 0 | ON/OFF | Reset | 0 | 0 | 0 | 0 | Reads the internal status BUSY 0: Ready 1: In operation ON/OFF 0: Display ON 1: Display OFF RESET 0: Normal 1: Reset |
| Set Address (Y address) | 0 | 0 | 0 | 1 | Y address (0~63) | Sets the Y address at the column address counter |
| Set Display Start Line | 0 | 0 | 1 | 1 | Display start line (0~63) | Indicates the Display Data RAM displayed at the top of the screen. |
| Set Address (X address) | 0 | 0 | 1 | 0 | 1 | 1 | 1 | Page (0~7) | Sets the X address at the X address register. |
| Display On/off | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0/1 | Controls the display ON or OFF. The internal status and the DDRAM data is not affected. 0: OFF, 1: ON |

- Display On/Off

The display data appears when D is 1 and disappears when D is 0.
Though the data is not on the screen with D=0, it remains in the display data RAM.
Therefore, you can make it appear by changing D=0 into D=1.

| RS | R/W | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | D |

- Set Address (Y Address)

Y address (AC0~AC5) of the display data RAM is set in the Y address counter.
An address is set by instruction and increased by 1 automatically by read or write operations of display data.

| RS | R/W | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 1 | AC5 | AC4 | AC3 | AC2 | AC1 | AC0 |

- Set Page (X Address)

X address (AC0~AC2) of the display data RAM is set in the X address register.

Writing or reading to or from MPU is executed in this specified page until the next page is set.

| RS | R/W | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 1 | 0 | 1 | 1 | 1 | AC2 | AC1 | AC0 |

- Display Start Line (Z Address)

Z address (AC0~AC5) of the display data RAM is set in the display start line register and displayed at the top of the screen.
When the display duty cycle is 1/64 or others (1/32~1/64), the data of total line number of LCD screen, from the line specified by display start line instruction, is displayed.

| RS | R/W | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 1 | 1 | AC5 | AC4 | AC3 | AC2 | AC1 | AC0 |

- Status Read

| RS | R/W | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0 | BUSY | 0 | ON/OFF | RESET | 0 | 0 | 0 | 0 |

- BUSY
When BUSY is 1, the Chip is executing internal operation and no instructions are accepted.
When BUSY is 0, the Chip is ready to accept any instructions.

- ON/OFF
When ON/OFF is 1, the display is on.
When ON/OFF is 0, the display is off.

- RESET
When RESET is 1, the system is being initialized.
In this condition, no instructions except status read can be accepted.
When RESET is 0, initializing has finished and the system is in the usual operation condition.

- Write Display Data

Writes data (D0~D7) into the display data RAM.
After writing instruction, Y address is increased by 1 automatically.

| RS | R/W | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |

- Read Display Data

Reads data (D0~D7) from the display data RAM.
After reading instruction, Y address is increased by 1 automatically.

| RS | R/W | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |

# Text boxes

OUTPUT

30pF